# https://esp3d.io/esp3d-tft/v1.x/hardware/sunton-43-8048/index.html

# 4.3' ESP32-8048S043C
- ESP32-S3 based + SDReader + PSRAM + 4.3’ IPS TFT (800x480) with Capacitive touch screen
  - Aliexpress
## Features
- ESP32-S3 dual-core Xtensa 32-bit LX7 microprocessor, up to 240 MHz with 384KB ROM, 512KB SRAM. 2.4GHz WiFi and Bluetooth 5
- FLASH: 16MB
- PSRAM: 8MB
- Micro-SD card slot (SPI)
- 4.3-inch 800x480 IPS TFT display - ST7262 (Parallel RGB-565 interface)
  - (https://lang-ship.com/blog/work/esp32-4827s043/)
- Capacitive touch panel - GT911 (i2C - 0x5D or 0x14)
- 1 USB-C to Serial 0 (CH340C)
- I2C / SPI / GPIOs
- Boot and reset buttons
- Dimension: 181.0mm x 108.0mm
- Header P1 (4 pins) (UART): Gnd, Rx, Tx, +5V
- Header P2 (4 pins) (SPI): IO13, IO12, IO11, IO19
- Header P3 (4 pins) (USB/UART): IO20, IO19, IO18, IO17
- Header P4 (4 pins) : IO18, IO17, +3.3v, Gnd
## Pins
Pin	Usage
GPIO 0	BOOT_BTN
GPIO 1	LCD_B4
GPIO 2	TFT_BL
GPIO 3	LCD_B1
GPIO 4	LCD_G5
GPIO 5	LCD_G0
GPIO 6	LCD_G1
GPIO 7	LCD_G2
GPIO 8	LCD_B0
GPIO 9	LCD_B3
GPIO 10	SD_CS
GPIO 11	SD_MOSI
GPIO 12	SD_SCK
GPIO 13	SD_MISO
GPIO 14	LCD_R4
GPIO 15	LCD_G3
GPIO 16	LCD_G4
GPIO 17	NC
GPIO 18	CTP_INT*
GPIO 19	CTP_SDA
GPIO 20	CTP_SCL
GPIO 21	LCD_R3
GPIO 33	NA
GPIO 34	NA
GPIO 35	NC / NA
GPIO 36	NC / NA
GPIO 37	NC / NA
GPIO 38	CTP_RST
GPIO 39	LCD_HSYNC
GPIO 40	LCD_DE
GPIO 41	LCD_VSYNC
GPIO 42	LCD_PCLK
GPIO 43	U0TXD
GPIO 44	U0RXD
GPIO 45	LCD_R0
GPIO 46	LCD_B2
GPIO 47	LCD_R2
GPIO 48	LCD_R1

* Requires Hardware Mod
### Hardware Mod (Add Hardware Interrupt for GT911)
NOTE: This only applies to the screen with the Capacitive touch panel (ESP32_8048S043C)
By default, this board does not connect the Capacitive Touch Screen’s GT911 Interrupt pin to any GPIO pins. This means that the code has to use polling instead of hardware interrupts to determine when the screen is being touched. This results in excessive CPU utilization of greater than 80%. Making the below modifications results in a significantly reduced CPU utilization of under 10% on avg (on static screens).
#### Steps (see picture)
- Install a 0 ohm resistor or solder bridge across R17. This connects the GT911’s INT pin to GPIO18.
- (If installed) Remove (pull-up) resistor R5 (GPIO18 to 3V3). The GT911’s INT pin is not strong enough to drive GPIO18 low with this resistor installed.
- (If installed) Remove U1 (XPT2046). This is not needed for the Capacitive touch panel and may conflict with GPIO18 if left on the board.
NOTE: Remember to enable the HARDWARE_MOD_GT911_INT option in CMakeLists.txt